### Instructions for re-stringing pleated fabric day/night shades

Pry loose the end caps on all rails with a flat head screwdriver or pocket knife. The rails slide off horizontally, and may get hung up on a knob rivet, so be firm, it will eventually slide off.

In the top rail, the cord will be attached to a spring on each side. The cord coming from the left will run down through the left side of the night material. The cord coming from the right will run down through the right side of the night portion of the shade.

The cords will cross in the center rail, so that the cord that runs down the left hand portion of the night shade, will cross over and run down through the right hand side of the day shade. Do the same for the right hand side of the night shade. It will cross over in the center rail and run down through the left hand side of the day shade.

Hang in there, you’re almost done!!

Now the cord coming down through the right side of the day portion will once again cross in the bottom rail and exit out of the left hand side of the shade through the end cap. Do the same with left hand day portion of the shade. Slide the bottom rail back on and then re-insert the end caps.

REMEMBER: Reset the drop of your shade by tying the cord retainers where you need them to be and adjust the tension as needed by wrapping the cord around the cord retainers.

(This information was sent to us by United Shade, LLC---28605 C.R. 8---Elkhart, IN 574-262-0954)

------------------------------------------------------------------------------------------------------------------------------------------

Good site:   http://www.fixmyblinds.com/instructions-09.html

|  | Home How to Order Blind Repair Products String Size Help Page All Products Instructions Glossary of Terms Shopping Cart Clearance Bin Testimonials About Us F.A.Q.'s E-mail Links | Restring Instructions for: Cellular Shades (Standard) Honeycomb Shades (Standard) Pleated Shades (Standard) Purchase Items for Repair NOTE: These directions are for the most commonly sold cellular shades. The instructions will work for most other cellular/honeycomb shades and pleated shades. Some cordlocks may be underneath or on the front of the headrail and may require fewer or more steps to complete the repair. Step 1) Remove the rails from the fabric (Figure 1). Slide the rails off the end of the fabric opposite the cordlock. Notice that only the top and bottom cells of the fabric stack fit inside the rails. These cells are reinforced with an aluminum slat or a stiff plastic material, called "filler strips". Important: Do not remove or change the position of the filler strips. Figure 1 Step 2) Pull the washers and cord lengths from the bottom of the fabric stack. Discard the string and save any other parts. You may need to reuse them. Step 3) If the cord guides (Figure 2) are worn, rotate them 180 degrees so that you can use the unworn edge. You may need to swap them with the ones that are inside the bottom rail. The cord guides fit through the holes in the top cell and filler strip. The cord guides should align with the edges of the fabric. Figure 2 Step 4) Measure and cut one cord length for each rout hole in the shade. The length of each new cord should be equal to TWICE the shade height plus the shade width. Step 5) Thread the cord through the eye of the restring needle. Gently push the needle through the cord guide and rout holes in the fabric stack (Figure 3). Once the needle is through the bottom part of the fabric and cord guide pull it from the bottom. Repeat this procedure for each cord rout hole. Figure 3 Step 6) Tie a plastic washer onto the bottom end of each cord. The washer prevents the cord from slipping back through the fabric stack. Tie a triple knot below the washer as shown (Figure 4). Any excess cord will be hidden when the bottom rail is re-installed. Pull the cord from the top of the fabric to make the washer snug against the bottom. Figure 4 Step 7) Slide the bottom rail onto the bottom cell and filler strip. The cell fits into the large opening in the rail, called the fabric channel (Figure 5). Be careful not to snag the fabric when sliding on the rail. Step 8) Slide the headrail onto the top cell and filler strip (Figure 5). Run the cords along the center of the top cell toward the cordlock side of the fabric stack. Keep the cords neat and do not cross them. Maintain a slight tension on the cords when sliding on the rail, and make sure the tops of the cord guides remain straight. Again, be careful not to snag the fabric. Figure 5 Step 9) By hand, thread the cordlock with its attached cover. Insert the cord through the bails and out the bottom of the cordlock. With cordlock "A": At the top of the cordlock, route the cords along the cord channel out the end of the cordlock (Figure 6). Figure 6 (Cordlock A) With cordlock "B": At the top of the cordlock, route the cords under the plastic tab and out the end (Figure 7). Figure 7 (Cordlock B) Note: The cordlocks shown here are just a sample of the most common ones on the market. Your cordlock may look different and may require additional steps to complete the repair. Step 10) Install the cordlock and end cap onto the rails (Figure 8). Push the end cap securely onto the bottom rail. Slide the cordlock with its attached cover along the cords to the end of the headrail. Push the cordlock onto the headrail, keeping tension on the cords to avoid pinching or twisting them. This procedure is the same for both cordlocks "A" and "B". Figure 8 Step 11) Re-install the shade assembly. Be sure the cordlock is locking the cords to hold the fabric compressed. With the cordlock facing you, slip the headrail into the installation brackets (Figure 9). The front lips on the brackets fit into the front groove on the top of the rail. Push on the rail until it snaps into place. Make sure that no fabric is trapped between the back side of the headrail and the tabs on the installation brackets. Use a screwdriver to tighten the tab screw on each bracket until it is just snug. Important: Do not overtighten the screws. Figure 9 Step 12) Install the equalizer onto the lift cords (Figure 10). The bottom rail should be raised all the way and the cords should be hanging freely from the cordlock. The equalizer will be placed on the strings about where the bottom rail will rest. Note: Your shade may be equipped with just an equalizer or it may use some other type of device, such as a metal ball joiner (See Step 15), to connect the lift cords to a larger diameter pull cord. Figure 10 Step 13) Adjust the shade assembly. Lower the shade until it is completely extended to the desired length. Loosen the equalizer by holding the cords and sliding the body upwards to release the wedge. Level the bottom rail by pulling on each cord individually, or adjust the shade drop by moving the cords as a group. Then, while holding the lift cords at equal tension, move the equalizer body against the cordlock and slide the wedge securely into the body making sure the locking tab is against the cords holding them securely in place. After double-checking that the bottom rail is at the desired position, lock the wedge in place by pushing it against a flat surface until it is flush with the body. Important: Be sure not to cross the lift cords; if crossed, the wedge cannot adequately secure them. Step 14) Tie on the tassel (Figure 11). With the shade closed, thread the cords through the tassel and tie a double knot in the cords (you may need to use a plastic washer) where you want the tassel to hang. Typically, this is about two-thirds down the shade from the cordlock. Keep the cords taut when you tie them to avoid any slack. Trim off the excess cord. Figure 11 Procedures When a Ball Condenser Is Used Step 15) (Optional) Disassemble the ball condenser. Insert the lift cords through one end and place a plastic washer on the cords. Tie a knot in them once the shade is in the proper position. Do not cut the cord until you make sure the shade raises and lowers evenly and completely. Trim the lift cord leaving about one half of an inch remaining below the knot. Attach the pull cord through the other end of the metal ball and tie a knot in it. Attach the tassel to the other end (Figure 12) of the pull cord. Figure 12 Use this diagram to configure the cords for a metal ball condenser. |
| --- | --- | --- |
|  | Home ¦ How To Order ¦ Blind Repair Products ¦ All Products Restring Kit Help ¦ Blind Repair Glossary ¦ Instructions ¦ Testimonials About Us ¦ Printable Order Form ¦ Secure Order Form ¦ Shopping Cart F.a.q. About Blind Repair ¦ E mail ¦ Links ¦ Site Map How Difficult Will The Blind Repair Be ? ¦ Security, Privacy, Warranty, & Delivery String Size Visual Helper ¦ Clearance Bin For more information: Fix My Blinds Inc. 2343 Jet Wing Drive Colorado Springs, CO 80916 US Email: webmaster@fixmyblinds.com (719) 597-0696 Fax: 866-550-6115 Day n Nite repair: Irvine Shade & Door 940 Challenger St Brea, CA 92821-2930 |

Rainbow Shades" in Goshen, Ind, Ph. (574)875-6162. They fix all brands, $25 each, with quick turn around. Nice people, give them a call.

Specialty Window Coverings 
1655 Gateway Ct. 
Elkhart IN 46514 
(574)262-5190

------------------------------------------------------------------------------------------------------

Irvine Shade and Door, Inc 
1000 Verdant DR 
Elkhart, IN 46516 
(574) 522-1446 
(574) 522-0568 FAX 

or 

961 Via Rodeo 
Placentia, CA 92870 
(714) 630-1927 
(714) 630-1957 FAX

Tag on our shade in bedroom (side):

“Pleated shades by EDI

Elkhart ind, Anaheim CA

RV Interiors 7 apr 92

EDI ref PIS 373

CRE Peach

PO 0311    Size 63X31”